## Slide 1: STM32 Training IoT Module
August, 2021

## Slide 2: Giới thiệu
MQTT Protocol Stack
ESP-LINK Integration
Setup Mosquitto Broker
Setup MQTT Client Box
SLIP Protocol

## Slide 3: MQTT Protocol
MQTT = Message Queuing Telemetry Transport

## Slide 4: MQTT - Message Flow

## Slide 5: MQTT - QoS (Quality of Service)

## Slide 6: ESP-LINK STM32 Integration
Note: dùng riêng dây usb cấp nguồn cho ESP + nối thêm dây bus GND)

## Slide 7: ESP Module

## Slide 8: ESP-Link Firmware
ESP-Link
https://github.com/jeelabs/el-client
Prequisite:
- Python 3 (3.7, 3.8, 3.9)
- Install esptool.py
python .\setup.py build
python .\setup.py install
OR
pip install esptool

## Slide 9: Command line tool
Edit COM Port
esptool.py --port COM14 erase_flash

## Slide 10: ESP-Link: Setup Wifi
Step 1: join ESP AP Wifi – press Connect
Open Browser ESP’s IP:
192.168.4.1

## Slide 11: Setup Station Mode

## Slide 12: Modem setting

## Slide 13: Setup MQTT Link
Reboot after changes

## Slide 14: Cài đặt MQTT Broker
Chú ý: Mở Task Manager, tìm server “mosquito” sau đó click chuột phải, nhấn Stop trước khi chạy.

## Slide 15: Cấu hình MQTTBox
127.0.0.1:1884

## Slide 16: Pub/Sub dùng MQTTBox
Chú ý:Các client phải cùng publish/subscribe trên cùng 1 topic name mới có thể gửi/nhận dữ liệu với nhau.

## Slide 17: SLIP Protocol (1)
SLIP = Serial Line IP
Break an IP datagram into bytes
Send the END character after the last byte (before the first byte as well)
Replace any data byte “C0” with “DB DC”
Replace any data byte “DB” with “DB DD”

## Slide 18: SLIP Protocol (2)

## Slide 19: ESP-Link Frame Structure (1)
Sent from STM32
CMD = Command ID
Value = Depend on CMD (Callback Address)
ARGC = Argument Count
DATA 0 .. DATA N-1: Argument Data

## Slide 20: ESPLink Frame Structure (2)
Sent from ESP
CMD = Command ID (2 bytes)
ARGC = Argument Counts (2 bytes)
Value = Depend on CMD (Function Callback Address) ( 4 bytes)
DATA 0 .. DATA N-1: Argument Data Bytes

## Slide 21: Reference Resources
1. Hướng dẫn cài đặt mosquito broker
https://m2msupport.net/m2msupport/install-mqtt-broker-mosquitto-in-windows/
2. MQTT protocol
https://m2msupport.net/m2msupport/how-mqtt-works/
3. SLIP Protocol
http://www.tcpipguide.com/free/t_SerialLineInternetProtocolSLIP-2.htm

## Slide 22: THANK YOU!